## Slide 1: Oslc Product Domain
January 2023
PTC

## Slide 2: Agenda
Windchill PLM configuration management practices (20 mins)
Summary of current PTC implementation (15 mins)
Feedback and Current limitations (15 mins)

## Slide 3: PLM – HOLISTIC Product Definition
Parts are the foundation for product definition in the Digital Thread
Enable associations to
  CAD (MCAD/ECAD)
  Documents
  Visualization
  Dynamic Documents
  Change processes
  Quality processes
  Requirements & System Models (OSLC)
  Process Plans
  And more…
Used By
Uses
Part 123 - A.2 (In Work)
And can be associated to
CAD Documents
Change Items
Documents
Dynamic Documents
Requirements (OSLC)
Process Plans
Related to

## Slide 4: Configuration Management – PLM Concepts
123
B.2
123
A
123
A
What is a Part Master?
  A database object that records information about Parts that does NOT change with the creation of new revisions
What is a Part Version?
  A database object that records information unique to a specific point in a Part’s design life cycle
  Caries a version designator such as “A” or “1”
  References Windchill Documents which are unique to that version such as:
    Specifications
    CAD models
123 – Part Name
A.3
123
123
A.3
123
B.2
Part Master
Part Versions
123 – Part Name
A.3

## Slide 5: PLM Configuration Management
How does Windchill know which Versions to show in the BOM?
Which of these Part Versions is the latest with state “Released?”
1
A
1
1
B
4
5
6
4
7
6
5
A
5
B
7
A
8
9
10
9
11
12
In Work
Released
Released
Released
In Work

## Slide 6: PLM Configuration Management
Which of these Part Versions is the latest with state “Released?”
1
A
1
1
B
4
5
6
4
7
6
5
A
5
B
7
A
8
9
10
9
11
12
In Work
Released
Released
Released
In Work
The product structure navigator walks from the top of the tree to the bottom, selecting the appropriate Part Version.

## Slide 7: PLM – Linking Data
Several common patterns to link related data in Windchill
Version Specific Relationships – “Described by”
  The Relationship holds information about the Versions on both sides of the link
  Making changes to the Versions requires explicit action – for example manual update, or update via change process
Version Independent Relationships – “References”
  The Relationship always points to the Latest Version of the related item
  The user will always see the latest version of this and does not have to do any additional actions
    Can use a Configuration Specification such as Baseline or Effectivity to determine a specific version (as long as there is a valid link)
There are other relationship types such as Master and Revision, but are not as common in these types of use cases

## Slide 8: Extending Concepts to OSLC Traceability
ALM applications in general support Branch and Copy models
MBSE tools have both concepts
  (Depending upon vendor and domain)
Trace links can have different behavior
  PTC will support the ability for configure Trace links to communicate configuration information
  A valid link must exist for configuration information to be valid between systems
Augment OSLC to communicate configuration information
Support updating links manually, via Change process or Programmatically
Enable additional configuration concepts to be supported
  Share Baseline information across systems
  Leverage concepts such as State or Effectivity where appropriate
Req 1, A-1
Req 1, B-1
Req 1, B-2
Part 1 (Master)
Rev A.1
Rev A.2
Rev B.1
Requirements Domain
Part/Product Domain
Change
Link is created / updated based upon explicit action such as a Change or via rules

## Slide 9: Effectivity
Determines when a Part Revision is planned to be ”Used in Production”
Three kinds of effectivity
  Date (global or effectivity context)
  Lot (requires effectivity context)
  Serial Number (requires effectivity context)
Able to enter both a beginning and ending parameter
  Date => 01/31/2009 – 12/31/2010
  Unit => 001-020
Configuration Specification used to expand a product structure according to effectivity

## Slide 16: PLM Linked Data
Version-To-Version Links
Describes
Reference
A.1
A.2
A.3
B.1
A.1
A.2
A.3
B.1
A.1
A.2
To Link to Version B.1 explicit action must be taken
B.1

## Slide 17: Agenda
Windchill PLM configuration management practices (20 mins)
Summary of current PTC implementation (15 mins)
Feedback and Current limitations (15 mins)

## Slide 18: Windchill as OSLC server
https://pwdcsv-wcqa54d.ptcnet.ptc.com/Windchill/oslc/catalog

## Slide 19: Windchill OSLC services
https://pwdcsv-wcqa54d.ptcnet.ptc.com/Windchill/oslc/catalog/config

## Slide 20: SEARCH FOR PARTS
https://pwdcsv-wcqa54d.ptcnet.ptc.com/Windchill/oslc/config/parts

## Slide 21: SEARCH FOR PART versions
https://pwdcsv-wcqa54d.ptcnet.ptc.com/Windchill/oslc/config/versionParts

## Slide 22: Reverse look-up service
https://pwdcsv-wcqa54d.ptcnet.ptc.com/Windchill/oslc/config/links/traceLinkResources?oslc.where=wnc:traceLinkTargetURI=https://ppuwsv-alm15t.ptcnet.ptc.com:9101/api/oslc/projects/5/rm/requirements/1274

## Slide 23: how Modeler OSLC Client links to Windchill PLM parts
  All Windchill Part versions are available for linking
  OSLC Links created using ‘parts’ will be version-independent
    i.e. always point to the latest version
  OSLC Links created using ‘part versions’ will be static and version-specific
    i.e. always point to a certain version
Part (defaults to latest version)
All part versions

## Slide 24: Agenda
Windchill PLM configuration management practices (20 mins)
Summary of current PTC implementation (15 mins)
Feedback and Current limitations (15 mins)

## Slide 25: Poor PLM COVERAGE IN OSLC
  No dedicated representation for PLM part information in OSLC (other than the Architecture domain which was deemed too generic)
    forcing vendors to use inappropriate OSLC domains
    which leads to poor quality data
    which leads to poor quality integrations

## Slide 26: Poor UX, Weak Support for CM
  PLM Parts and part versions are accessed one at a time
    Painful…
  No structure information served up
    Only see 1 small slice of the product
    OSLC lacks clarity on parent/child relationships for a eBoM view

## Slide 27: Weak Support for CM
  No configuration management-based filtering possible as PLM Config Mgmt concepts not supported in OSLC.
  Would like to be able to set the Configuration Specification when accessing a part structure via OSLC.
    Similar to setting the Global Configuration when accessing DOORS resources

## Slide 28: QUESTIONS?

## Slide 30: Config mgmt. - Modeler
Windchill Modeler items do not have a number or ID that is exposed to users
They are identified by the
  Type
  Name
  Scope (Package location)
  Full name (Scope.Name)
All model items (including packages and diagrams) have an internal ID called a GUID
  This is not directly visible to users

## Slide 31: Config mgmt. - Modeler
Windchill Modeler manages versions at the model level
  Individual items have versions, but are not exposed to users
The latest model version (also called the tip) is writable
Old versions are locked, and act as baselines

## Slide 32: Config mgmt. - Modeler
Windchill Modeler provides the ability to branch a model – called a private sandbox
Model items can be changed in isolation, then reconciled (merged) to the main model (trunk)

## Slide 33: Config mgmt. - Modeler
Windchill Modeler OSLC Server
  Exposes all model versions
    Use to create static, version specific OSLC Links
  Exposes current version (latest)
    Link to these items for an OSLC Link that always point to the latest
Windchill Modeler OSLC client
  Allows the creation of OSLC Links and OSLC Surrogates
  Several link types can be used
  Link direction can be specified (incoming, outgoing)